## Slide 1: Software is Energy Lean software for Green Computing
maurizio.morisio@polito.it
Notes: Giocare sul ?

## Slide 2: Kudos
Luca Ardito
Giuseppe Procaccianti
Antonio Vetrò

## Slide 4: Outline
Concepts
Facts
Guidelines
Roadmap
  Labels
  Essentials
Concepts
Facts
Guidelines
Roadmap

## Slide 5: Concepts

## Slide 6: Green what?
System
Software process
Software product
Embedded Software product
Greening software (ICT)
Greening by
Software (by ICT)
Greening the process
Notes: Options: green the process (not much leverage)
green the sw product
green the system

## Slide 7: Effects
Socio technical System
System
Software process
Software product
Embedded Software product
First order
Second order
Third order
Notes: Ex first order. Hardware consumes less, because of better algorithm
Ex of second order. Car consumes less fuel, thanks to better routing (ICT) or better negine management
remark, sw can be ineffcientt bu tsystem more efficient
Ex of third order. People use car less because of ICT devices that show consumptions / emissions

## Slide 8: Greening ‘by’ software
Smart grids
Smart cities
Smart cars
Smart factories
Smart ..

## Slide 9: Greening ‘by’ software
The world is my energy oyster
Notes: The world is my oyster (enjoy the world – the world is the limit to green by sw)

## Slide 10: Greening ‘the’ software
development
operation
maintenance
deployment
dismissal
Green the process
(LEAN and GREEN)
zero order effect
Green the software
First order effect
Notes: Paper su distribuz TCO per PC? Qui operation conta poco

## Slide 12: Green, what?
What does software mean exactly?
Energy Consumption / Waste / Gas emissions
  ISO 14040, LCA
Sustainability
  ISO 25010 (was ISO 9126) extended

## Slide 13: Life Cycle Assessment – ISO 14040
Notes: Flows: energy, water, gas emissions, wastes, raw materials
Sort of TCO for energy
In cars, well to wheel
Example of electric cars

## Slide 14: LCA
Flows
  Energy
  Gas emissions
  (raw materials and wastes)

## Slide 15: Sustainability
“meeting the needs of the present without compromising the ability of future generations to meet their own needs” [UN report]
Dimensions
  Economic
  Social
  Environmental
  Technical
  (Human)
Notes: United Nations. Report: Our Common Future. In Conference on Environment and Development, 1987.

## Slide 16: ISO 25010
Energy efficiency
Notes: Ardito L., Procaccianti G., Vetro' A., Morisio M. Introducing Energy Efficiency into SQALE in ENERGY 2013, The Third International Conference on Smart Grids, Green Communications and IT Energy-aware Technologies

## Slide 17: ISO 25010
Sustainability
In use
Energy consumption
Energy efficiency
Pollutant emissions

## Slide 18: Metrics
Sustainability
  Environmental dimension
    Energy [Joule]
    Power [Watt]
    Efficiency: useful energy / total energy
    Productivity: computational work / energy

## Slide 19: Metrics
NODE
NETWORK
INFRASTRUCTURE
Notes: Ardito L., Morisio M. Green IT - available data and guidelines for reducing energy consumption in IT Systems SUSTAINABLE COMPUTING, Vol.4, pp.24-32, ISSN:2210-5379

## Slide 20: Node
Application
OS
Hardware

## Slide 21: Metrics – node level
Power, Energy:
  Watt, Joule
Productivity:
  MFLOPS / Watt
Power (node/application):
  power used by application
Productivity (node/application):
  sorted records / Joule
Power (node/OS):
  power used by OS

## Slide 22: Metrics - network
Efficiency (network):
  energy(full - idle)/energy(full)
Productivity(network):
  KB transferred / Joule

## Slide 23: Metrics – infrastructure level
Productivity (data center):
  useful work / energy
Efficiency (data center):
  power used for storage /total power used

## Slide 24: Summary
(Zero), first, second, third level effects
Green? Sustainable?
No established general model
  Suggestion, first level
    25010 extended with sustainability in use,
    metrics like energy, power, efficiency, productivity
    At node/network/infrastructure level
  LCA to be included
    Assumption: operation phase counts most

## Slide 25: Outline
Concepts
Facts
Guidelines
Roadmap
  Labels
  Essentials
Concepts
Facts

## Slide 26: Facts

## Slide 27: Energy consumption (2007)
Chart: 
| Energy consumption [TWh] | Electrical energy consumption | ICT EE consumption
 | 122600 | 16570 | 830
TOTAL: 144000 TWh

## Slide 28: Energy consumption (2007)
Socio technical System
System
Software product
Embedded Software product
First order
Second order
Third order
1% total E (14000 TWh)
5% total EE (17400 TWh)
Notes: J. Bogdanovic, C. Heberlein, O. Simonett, and C. Stuhlberger “Kick the Habit: A UN Guide to Climate Neutrality,” PROGRESS PRESS LTD MALTA, 2008.
M. Webb, E. Al., Smart 2020: Enabling the low carbon economy in the
information age, The Climate Group London (2008).

## Slide 29: Energy consumption within ICT
Chart: 
| Data Centers [TWh] | PC [TWh] | Laptops | Mobile Phones | Network
 | 330 | 163.2 | 46.2 | 44.6 | 6.05
Notes: Focus on data centers, but not only

## Slide 30: CO2 emissions
Socio technical System
System
Software product
Embedded Software product
First order
Second order
Third order
2% total emissions
Notes: J. Bogdanovic, C. Heberlein, O. Simonett, and C. Stuhlberger “Kick the Habit: A UN Guide to Climate Neutrality,” PROGRESS PRESS LTD MALTA, 2008.
M. Webb, E. Al., Smart 2020: Enabling the low carbon economy in the
information age, The Climate Group London (2008).

## Slide 31: CO2 emissions, ICT
Chart: 
| PCs | Telecommunications | Data centers [MtCO2]
 | 200 | 150 | 76

## Slide 32: Lifecycle analysis - PC
Chart: 
| Design Manufacture [MJ ] | Transport | Purchase Use | Other
 | 4250 | 950 | 1500 | 1200
Notes: E. Williams, Energy intensity of computer manufacturing: hybrid as-
sessment combining process and economic input-output methods., En-
vironmental science technology 38 (2004) 6166{6174.
[32] V. G. Moshnyaga, A new approach for energy management in user-
centric applications, in: Proceedings of the International Conference on
Green Computing, GREENCOMP '10, IEEE Computer Society, Wash-
ington, DC, USA, 2010, pp. 107{112.

## Slide 33: Energy– data centers
Chart: 
| Servers [MJ] | Power and cooling infrastructure | Power | Other infrastructure
 | 174.9 | 75.9 | 62.7 | 16.5
Notes: V. G. Moshnyaga, Integrated circuit and system design. power and
timing modeling, optimization and simulation, 2009, pp. 82{92.

## Slide 34: ICT footprint
Small in %
Big in absolute numbers
Increasing trend
Worthwhile to work for reducing it

## Slide 35: Software is energy?

## Slide 36: Software is energy?

## Slide 37
idle
Web nav
Email
Product suite
Disk access
USB access
Video play
P2P
Skype call
Audio play
Skype call video
Image browsing
Notes: 10 20 % (+10W 50 to 60 blue, 86 96 red)
Procaccianti G., Ardito L., Vetrò A., Morisio M. (2012)

## Slide 38
Web nav
Email
Product suite
Disk access
USB access
Video play
P2P
Skype call
Audio play
Skype call video
Image browsing

## Slide 39: PC, application families
Notes: The Impact of User Choice on Energy Consumption
Chenlei Zhang, Abram Hindle
Daniel M. German

## Slide 40: Issues
Definition of scenarios of usage
Measurement and effect of context
  (In)dependence of hardware
  (In)dependence of other applications

## Slide 41: Summary
Small % consumption of ICT, but huge in absolute number, and increasing
Servers first, then PCs, mobile phones
In lifecycle, manufacturing matters more
Application consumption can be measured, and has impact

## Slide 42: Outline
Concepts
Facts
Guidelines
Roadmap
  Labels
  Essentials
Concepts
Facts
Guidelines

## Slide 43: Guidelines

## Slide 44: Guidelines
NODE
NETWORK
INFRASTRUCTURE

## Slide 45: Guidelines – node /application level
Efficient UI design
  To minimize time (energy) to accomplish a task
Event based programming
  No polling, no idle resources
Low level programming
  Virtual machines, high level programming may be energy inefficient
Batch I/O
  Economy of scale. OS can power down IO devices when not used

## Slide 46: Guidelines – Node/ application level
Allocate data / computation where more energy efficient
  Cfr deploy on cloud
Data redundancy and migration
  May reduce energy efficiency
Adapt/ scale QoS to energy availability
Use energy models
  To adapt / optimize behavior of application

## Slide 47: Guidelines – Node/OS level
Provide energy management services / API
  Cfr energy models for applications
Optimize use of devices
  Require collaboration from device drivers / device manufacturers
Use compiler optimization
Use only required services and background processes

## Slide 48: Guidelines – Node/ hardware level
Power down / optimize use of peripherals
Use special purpose hardware
Use dynamic power management capabilities
  ACPI
Devices provide energy consumption data
Notes: Advanced Configuration and Power Interface (ACPI)

## Slide 49: Guidelines – network level
Lower data traffic
Optimize protocols on energy consumption

## Slide 50: Guidelines – infrastructure level
Deploy applications on the cloud
  Virtualization, less hardware, less consumption
  Worse response times
Load balancing
  Distribute load on resources (CPU, storage ..)
  Less powerful hardware needed
Make information about consumption available
  For adapting energy behaviour

## Slide 51: Guidelines - summary
Adaptation
  feedback loops on energy /power
  availability of energy information
  models for energy behavior
  scenarios of energy usage
    Works already at OS – device level, to be extended upwards
System thinking
  Allocation of data/computation in function of (system) energy consumption

## Slide 52: Outline
Concepts
Facts
Guidelines
Roadmap
  Labels
  Essentials
Concepts
Facts
Guidelines
Roadmap

## Slide 53: Roadmap

## Slide 54: Research goals
Concepts
  Greening software or by software???
  Agreed upon high level model (25010 ..)
Facts
  Productivity and efficiency figures
  Application level
Guidelines
  More detailed
  With context (AKA patterns and antipatterns)
  With quantified effects

## Slide 55: Research goals
Guidelines
  Availability of energy / power / usage information at all levels
    Hardware, OS, application, function
  Definition and validation of energy models at all levels
  Self adaptation, at all levels
    System level, layered
  Benchmarking

## Slide 56
Figura label lavatrice

## Slide 57: Software Energy Labels
scenarios
Measurement standards
A
C
B
D
benchmark
application
class

## Slide 58: Software Energy Labels
assess
application
class
refactor
guidelines

## Slide 59: Well..
Interest in domain is raising
  Workshops, journals..
‘Greenness’ as (yet another) NF requirement (aka safety security) probably to stay
Lot of work to be done..
  Define guidelines (good practices for software energy efficiency)
  Quantify actions (guidelines) in terms of results
  Trace energy efficiency to process / product

## Slide 60
Have an energy (and brain) efficient workshop